## Slide 1: Recap SW5 - RTOS
Kilian Ineichen und Silvano Stecher

## Slide 2: RTOS Why RTOS?
Solves synchronization problems
Quasi-concurrent execution of services
Close to Hardware  better performance
  OS needs Driver
  RTOS direct connected
  Correct Result at correct time, independent of System load, in a deterministic and foreseeable way
Requirements for standard OS and RTOS are different

## Slide 3: RTOS Kernel
Catching Interrupts
Time base (Timer/Tick Interrupt)
System Call and Traps (Trigger Interrupt)

## Slide 4: RTOS Scheduler
Tick passes control to scheduler
Scheduler can schedule other Task
Opportunities: Tick, Wait(), Yield(), Sync()

## Slide 5: RTOS OS Process States
Only one Task running

## Slide 6: FreeRTOS Architecture
Kernel
  Small Kernel, implemented in C
  Preemptive or cooperative scheduler mode (at compile time)
  Kernel only needs tick interrupt and software interrupt
  ’Ticks’ provide time base for RTOS (Typically 10 ms or 1 ms tick period)
Notes: Bis hier Silvano

## Slide 7: FreeRTOS Architecture
Tasks
  Tasks are running with stack in the ’heap’
  Tasks are (usually) staying in an endless loop
  Software interrupt used to switch task context

## Slide 8: FreeRTOS Kernel Control
Starts the scheduler ( Init -> Running)
Creates IDLE task (configMINIMAL_STACK_SIZE, tskIDLE_PRIORITY)
Runs the highest priority task

## Slide 9: FreeRTOS Kernel Control
Puts the kernel from Active to Suspended state
Puts the kernel from Suspended to Active state

## Slide 10: FreeRTOS Kernel Control
  Forces a context switch with Software Interrupt
  Required for cooperative multitasking

## Slide 11: FreeRTOS Tasks
Preemptive Scheduling
  Always run the highest-priority ready task
  Multiple tasks with the same priority: time-slicing

## Slide 12: FreeRTOS Tasks
  vTaskDelay() => blocked

## Slide 13: FreeRTOS Task creation

## Slide 14: FreeRTOS Task

## Slide 15: Questions:
What does RTOS mean?
  Real Time Operation System
What are Pros and Cons for using RTOS in PREN?
  + Quasi-concurrent
  - Uses more Memory
What is Preemptive Scheduling?
  Multiple tasks with the same priority: time-slicing
  Always run the highest-priority ready task

## Slide 16
How can a Task force a context switch ( switch Task )?
  taskYield
How can you prevent, that your Task ends?
  For(;;){}