## Slide 1: Recap SW5 - RTOS
Kilian Ineichen und Silvano Stecher

## Slide 2: Wieso RTOS?
Synchronisation
Quasigleichzeitig
Hardwarenahe  bessere Performance
  OS würde Treiber benötigen
  RTOS direkt mit Hardware
Low Power und geringe Bootzeit

## Slide 3: Scheduler

## Slide 4: RTOS Kernel

## Slide 5: OS Process States

## Slide 6: FreeRTOS Introduction
Open Source, free-of-charge
  OpenRTOS: commercial supported version
  SafeRTOS: special version dedicated to safety critical systems
Processor Expert component

## Slide 7: FreeRTOS Architecture
Kernel
  Small Kernel, implemented in C
  Preemptive or cooperative scheduler mode (at compile time)
  Kernel only needs tick interrupt and software interrupt
  ’Ticks’ provide time base for RTOS (Typically 10 ms or 1 ms tick period)
  RTOS creates and runs in IDLE task

## Slide 8: FreeRTOS Architecture
Tasks
  Tasks are running with stack in the ’heap’
  Tasks are (usually) staying in an endless loop
  Software interrupt used to switch task context

## Slide 9: FreeRTOS Architecture

## Slide 10: FreeRTOS Architecture
Kernel and Interrupts
  Tick Interrupt: SysTick
  Software Interrupt: SVCall, PendableSrvReq
  Other interrupts: under application control
  Do not call RTOS API from ISR
  using PRIMASK to mask interrupts
  configMAX_SYSCALL_INTERRUPT_PRIORITY

## Slide 11: FreeRTOS Kernel Control
Starts the scheduler ( Init -> Running)
Creates IDLE task (configMINIMAL_STACK_SIZE, tskIDLE_PRIORITY)
Runs the highest priority task

## Slide 12: FreeRTOS Kernel Control
Puts the kernel from Active to Suspended state
Puts the kernel from Suspended to Active state

## Slide 13: FreeRTOS Kernel Control
taskYield
  Forces a context switch with Software Interrupt
  I Required for cooperative multitasking

## Slide 14: FreeRTOS Tasks
Preemptive Scheduling
Always run the highest-priority ready task
Multiple tasks with the same priority: time-slicing

## Slide 15: FreeRTOS Tasks

## Slide 16: Fragen:
PREN  wieso sollte ein OS oder wiso sollte ein RTOS verwendet warden? Was spricht dagegen was dafür.